## Slide 1: Lecture 12 Input/Output (programmer view)
Computing platforms
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2018

## Slide 2: Memory-mapped input/output
Device can be mapped to memory address
In next semester we will see what “mapping” actually means
For now, let’s imagine that memory cell 0xf3 is not a memory cell
But a register of external device
When you read or write this register, device can perform some action
Or vice versa, when a device performs some action, data are written to the register (and you can read it later)

## Slide 3: Simple device – a keyboard
Actually, not so simple (schematics is present in CdM-8 book)
When you press the key, 7-bit ASCII code is written to latch register
And 8-th bit of the register is set to 1 (strobe bit).
When you (CPU) read the register (cell at 0xf3), strobe bit is cleared
This way you can know if the new key was pressed
Or the same key was pressed several times

## Slide 4: Things to consider
For memory-mapped I/O, CdM-8 reserves upper 16 bits of memory
This allows for 16 devices, or, more specifically, 16 I/O registers
Single device can have several I/O registers
Or two devices can share one address for their registers (e.q. one device maps register for write operations and another for reading)
We must move stack below i/o page before doing any push and pop
Use addsp, not 16 push commands!

## Slide 5: How to actually input the data?
ldi r0, 0xf3
while
ld r1, r0
tst r1
stays gt
wend
This is called busy wait

## Slide 6: Why busy wait is good?
It works even for simplest hardware (better ways require special hardware support)
It is simple to program and debug
It is fast

## Slide 7: Why busy wait is bad?
You cannot do anything else when busy waiting for a single event
You must adapt your code when you wait for several events
You cannot stop CPU while busy waiting
  For CdM-8, this is not a problem
  For real CPU, it leads to high power consumption and heating
  If all CPU cores of typical modern smartphone will busy wait, they will eat all the battery in < than a hour

## Slide 8: Interrupt
Interrupt is a hardware mechanism implemented in CdM-8 and most ”real” modern CPU
Interrupts allow hardware devices to call software routines
Typically, interrupt signals that device has some data for you
For example, keyboard has a new key pressed
Or network interface has a new data packet received
This is different from pure software call, but also very similar
Details are different between CPUs and systems
Let’s discuss CdM-8 interrupts

## Slide 9: Interrupts from software point of view
Every interrupt-capable device has unique number on range 0 to 7
Every possible value of device numbers selects a byte pair, called interrupt vector
By default, interrupt vectors are mapped to upper 16 bytes of memory
In Manchester architecture, these are same bytes as used for memory mapped I/O, so you cannot use all 7 interrupts and all 16 register addresses
In Harvard architecture, I/O is mapped to data memory, and vectors to program memory

## Slide 10: But what happens when interrupt occurs?
Device sets IRQ request on CPU input line
When CPU finishes every instruction, it polls IRQ request line
If interrupts are enabled (we will discuss this later), it retrieves device number
Then, instead of next instruction at mem[PC], ioi instruction is executed
  In some sence, ioi is “normal” instruction: it has an opcode, it can be inserted in a machine code and executed like any other command
  This is called “software interrupt”
But during interrupt, no ioi instruction is present at mem[PC]
But CPU behaves like it fetched this instruction

## Slide 11: Ioi instruction
Phase 1 decrement SP for stack push
Phase 2 store PC on stack; decrement SP for stack push
Phase 3 store PS on stack
Phase 4 fetch new PC value from vector’s first cell (0xf0 + 2R)
Phase 5 fetch new PS value from vector’s second cell (0xf1 + 2R)
It is similar to jsr, but two registers are saved (PC and PS)
You need to use rti instruction to return from ioi routine
And call target depends on hardware (device number R)
So you can write separate handler routine for every device

## Slide 12: What you can do in interrupt handler?
Typically, interrupt signals that device has some data for you
So you must retrieve the data
Some devices require further instructions, what to do next
For example, when you read data from the disk, you must tell the disk what sector to read or write next (or not tell anything and disk will be idle)
Then you must set some flags so main program will know the data are ready
Then you must return to main program (execute an rti instruction)
Or you can do something else
(we will discuss it in Operating Systems course)

## Slide 13: Why interrupts are bad?
They are asynchronous
They can occur in any moment of program execution
It is very easy to write a handler that can break a main program (damage its data)
And it is very hard to catch this condition by testing
So, there is a mechanism to disable interrupts (a flag in PS register)
Interrupt handling is a simplest (and historically first) form of parallel programming, and parallel programming has many pitfalls
And most of these pitfalls are hard to avoid
There will be courses on concurrency and parallel programming further in our curriculum

## Slide 14: Why interrupts are good?
You can handle several event sources at same time
You do not need to rewrite your program to add another event source
You can do something useful when waiting for an event
Operating systems use interrupts to implement multithreading and multitasking

## Slide 15: Ring buffer
A simple technique which helps to avoid many pitfalls of parallel (asynchronous) programming
We will hear about ring buffers and queues in Operating Systems course
Ring buffer is very easy to implement in assembler
In C course you’ve seen queue and stack on linked lists
In our course, we’ve seen stack implementation on array
Ring buffer is queue implemented on the array

## Slide 16: Ring buffer (continued)

## Slide 17: How it works?
When interrupt handler retrieves the data, it advances end pointer and stores the data. When array ends, it wraps over (this is why it’s called a ring buffer)
When main program processed the data, it advances head pointer (probably wrapping over) and retrieves the data
When head pointer meets end pointer, queue is considered empty (main program must wait using busy wait or wait instruction)
Instead of busy wait, main program can tell OS not to schedule it (but again this is topic of another course. We have no OS in our course)
When end pointer meets head pointer, queue is considered full (interrupt handler cannot store data and must drop new data)

## Slide 18: Ring buffers and queues are everywhere
Many smart peripherial devices have internal buffers or queues, so they can send interrupts not so often, and CPU can process their data in batches
Many things you will see in networks and operating systems (disc caches, pipes, sockets, network switches and routers) are ring buffers or queues or something built around a ring buffer or queue