## Slide 1: Lecture 13 Harvard architecture Coccone OS demonstrator
Computing platforms
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2018

## Slide 2: Harvard version of CdM-8
Harvard architecture = separate memory banks for data and instruction
Can be implemented as:
  One-bit address extension selecting code and data access (cheap and simple)
  Separate memory channels (buses) – expensive but boosts performance
  Memory buses of different width (example: Microchip PIC has 8-bit data and 14-bit instruction memory)
  Separate cache channels and caches, probably backed by same main memory actually used in some CPU
In CdM-8, first approach (bit extension) is used
One ISA-level change: ldc (LoaD Constant) instruction to read data from instruction memory

## Slide 3: Coccone: most advanced version of CdM-8
Extension of CdM-8 architecture and schematics intended to demonstrate basic concepts of protected-memory operating systems
In second semester we offer team project: actually building OS for this machine
But what we need to build an operating system?

## Slide 4: Processes (tasks)
Most (but not all) modern operating systems have concept of process
Process is a virtual machine (or a sandbox) with limited access, that runs in isolated memory space
Process virtual machine is NOT emulating full access to system hardware (unlike hypervisor virtual machines like VMWare or VirtualBox)
All programs you write in C programming course and most other programs you use (including CocoIDE) are designed to be run as processes and use operating system services to access hardware

## Slide 5: What we need to protect memory
Essentially, we need to catch every memory access for a running program
Catch all memory accesses programmatically
  In fact, we need to interpret entire machine code of your program
  This is called byte-level interpretation
  This is how cocoemu actually works
  Orders of magnitude slower than hardware interpretation
  Can be significantly sped up by JiT compilation
  JiT is what Java, C# and many hypervisor virtual machines actually do, but this is far beyond scope of our course

## Slide 6: Catch all memory accesses in hardware
Insert a hardware device (MMU for Memory Management Unit) between CPU and memory bank
Coccone is using one of simplest known types of MMU, known as memory banks
Coccone uses 3 previously unused bits in PS register as bank selector
In tome.pdf and in Logisim schemes it is also referenced as page
Bits 0-3 - CVZN flags, bit 7 - interrupt enable, bits 4-6 - selector
So, we can use 8 memory banks 256 bytes each
Actually, there are 10 banks, but more on this later

## Slide 7: Coccone memory subsystem

## Slide 8: Memory banks are not equal
Banks 0-3 are reserved for OS code (even simplest OS won’t fit in single bank)
When bank 0-3 is active, CPU switches to Harvard mode and can use special 9th bank of RAM for data
When bank 4-7 is active, CPU switches to Manchester mode and uses the same bank for code and data
Banks 4-7 are for [user] processes
Bank 10 is for memory-mapped I/O
This is controlled by VBR MMU register (byte 0xff of OS data/IO pages)

## Slide 9: VBR (Virtual Bank Register)
Not available in “user mode” (code banks 4-7)
Can select one of
  user mode banks,
  OS data bank
  I/O page
for data access in “system mode” (code banks 0-3)

## Slide 10: How to copy data from OS to user bank?
297 ldi r2,data.KBusr # memory bank
298 ld r2,r2 # r2=memory bank
299
300 ldi r0,MMU #r0-> MMU I/O reg
301 st r0,r2 # set data memory bank
302
303 st r1,r3 # set data memory bank
304 inc r1 # advance buffer pointer
305
306 clr r2 # MMU reset to page 0
307 st r0,r2 #

## Slide 11: But how to actually switch banks?
When we write to bank selector, this is indirect jump (PC now points to different bank but to same position in the bank)
One solution: place a same piece of code in every bank
This code will handle bank switching
This approach is used in many 8-bit CPU with memory banks
Actually, this is used in many OS for 32- and 64-bit CPUs. A
All OS for x86 are using this approach (OS kernel is mapped to same addresses in all processes)

## Slide 12: And how actually change bits 4-6 of PS?
We know only two instructions that load and store full PS register: ioi and rti
We can use rti to put arbitrary value in PS (push it and then rti)
But rti is also a control transfer (considering a previous slide, this is good!)
And you can use ioi to call procedures in other banks (just place right PS value at vector 0!)
(Actually, many OSes use software interrupts for system calls)
Also, special instruction osix with single operand (equivalent to ioi to vector 0, but bits 0-6 of new PS are taken from the operand)

## Slide 13: But how interrupts work in multibank system?
Where interrupt vectors are placed?
What happens to the stack?
Coccone always takes interrupt vectors from bank 0
But the vector contains a bank selector, so the handler can be placed in different bank!
Coccone stack pointer is shadowed
There are actually 8 stack pointers, one for every bank ==one per process
But during interrupts, SP[0] is always used, so placing ISR in other banks require extra work

## Slide 14: More on osix and rti
osix can select target bank and set flags in PS
Handler in the bank can use flags and conditional branches to decode syscall number
We can have 4x16=64 useful syscalls (pointing to OS code pages)
And also 64 useless syscalls pointing to user code pages
  Useless syscalls actually disturb system operation, so coccone is not as protected as “real” protected memory systems
rti can put arbitrary values to PS on return
Syscalls can use flags to indicate failure or success
Syscalls can pass parameters in registers
We’ve seen how syscalls can copy data to user space, so we can pass pointers as parameters