## Slide 1: Lecture 2 Platform 0 revisited
Computing platforms, semester 2
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2019

## Slide 2: XOR gate
4 NAND gates * 4 transistors each = 16 transistors

## Slide 3: XOR gate optimized on transistor level
At the core, we have symmetrical circuit which is not equivalent to one of basic gates
To have output=1, we need one of upper pairs open: (A&B’=1 | A’&B=1)
To have output=0, we need one of lower pairs open: (A&B=1 | A’&B’=1)
12 transistors

## Slide 4: XOR gate optimized: second try
Much harder to understand

## Slide 5: How it works?
Consider B=0
This closes T0 and T7 directly, and opens T1
Open T1 opens T3 and closes T6
Transistors T2,4,5,8 form a pair of NOT gates
Output will be (A0)=A
Case B=1 is described in tome.pdf

## Slide 6: Pass transistor logic (PTL)

## Slide 7: Floating signals
N-type truth table
P-type truth table
Generally, you should avoid floating input on transistor gates
Also, you should avoid connecting conflicting outputs
But connecting floating output to non-floating one is OK
Actually, NOT gate uses exactly this kind of connection

## Slide 8: Pull resistor
Gives sort of default value to circuit output
I.e. when output floats, pull resistor pulls it to 0
If we connect it to PWR, it will pull it to 1

## Slide 9: NAND gate using pull resistor

## Slide 10: Why not use pull resistors everywhere?
They are slow
They consume power

## Slide 11: Controlled buffer
This device allows to controllably pass X to Y
Actual buffers are bidirectional (signal and even floating value passes also from Y to X)
But Logisim simulates them as unidirectional
Smarter implementation known as transmission gate
Less signal degradation