## Slide 1: Lecture 3 Combinational units. Adders
Computing platforms, semester 2
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2019

## Slide 2: Some terminology
Combinational units: pure logical functions.
  Output depends only on input
  No side effect (except delay)
  Can be described by single logical expression
Sequential units: have internal state
  Output depends not only on the inputs
  Input can have side-effect (changing internal state)
  Require logical elements we did not study yet.

## Slide 3: Popular combinatory units
Decoder
  k inputs, 2k outputs.
  Interprets inputs as k-bit number n, sets n-th output to 1, all others to 0
  Standard decoders usually have “Enable” input. When Enable is down, all outputs are down
Multiplexer
  2k m-bit inputs and one k-bit selector input
  Connects n-th input to the output

## Slide 4: 2x4 decoder

## Slide 5: Multiplexer (mux)

## Slide 6: So, the adder
Two bit half adder
Adds two bits and produces result and carry bit
S=AB, Cout=A^B

## Slide 7: The full adder
Has three inputs: A, B, Cin
Also has two outputs: R and Cout
Can be constructed from two half adders

## Slide 8: Three-bit adder
Place three full adders in a row
Connect Cout0 to Cin1, etc
Sounds simple and good enough for Logisim
For real devices, carry must propagate from bit 0 to N
This design is known as ripple carry adder
Delay ~= O(N)
We discuss this later

## Slide 9: Logisim notation for repeating circuits

## Slide 10: How to deal with carry propagation delay?
A sequential adder.
  Carry propagation time for N-bit adder ~=N(delay of single adder)
  Why bother building N adders if they cannot actually work in parallel?

## Slide 11: Carry-save adder
Result is provided as two bits (carry not propagated)
10111010101011011111000000001101 + 11011110101011011011111011101111 = 21122120202022022122111011102212
To produce binary number, we still need to propagate carry
But we can add these saved-carry numbers without converting to binary
And propagate only on last stage
Carry-save adders are used in multiplicators, in cryptography, etc

## Slide 12: Carry-lookahead
Instead of Cout, every adder provides two signals, P (propagate) and G (generate)
P(A,B)=AvB
G(A,B)=A^B
Ci+1=Giv(Pi^Ci)
Actually, a recursive formula
C4=G3v(P3^G2)v(G1^P2^P3)v (G0^P1^P2^P3)v(C0^P0^P1^P2^P3)
Gate count O(N2), but delay close to constant

## Slide 13: 4-bit carry lookahead in Logisim
Delay depends on number of gates the signal passes between input and output
NOT on total number of gates
In this design, C3 produced from 7 input signals, but each of these signals pass only two gates
So, we can improve speed by increasing number of gates
In computing, simpler is not always better

## Slide 14: Ways to produce multibit adder
Often, a combination of ripple carry and carry lookahead is used
16-bit adder can be implemented from 4-bit units as:
  ripple-carry connected via carry-lookahead
  carry lookaheads connected via ripple carry
  carry lookaheads connected via second level carry lookahead
Other tricks, like carry-skip (aka carry bypass) adder
  Read the Wikipedia…