## Slide 1: Lecture 4 Sequential units. Registers
Computing platforms, semester 2
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2019

## Slide 2: Some terminology
Combinational units: pure logical functions.
  Output depends only on input
  No side effect (except delay)
  Can be described by single logical expression
Sequential units: have internal state
  Output depends not only on the inputs
  Input can have side-effect (changing internal state)
  Depend on timing
  Require triggers, latches and memory

## Slide 3: Some final words on combinatory circuits

## Slide 4: Implementing arbitrary truth table
Draw input lines. Also add inverted lines
For every row yielding 1, add AND gate and connect it to corresponding input lines (may be to inverted one)
Connect outputs of AND gates to OR gate
This is called minterm approach (normal disjunctive form)
FPGA design tools do this automatically
Optimization steps (optional)
  If table has more rows yielding 1 than 0, build device for inverted table and invert the output
  Delete unused direct or inverted input lines

## Slide 5: Edge detector
One of the simplest sequential devices
Detects input transition from low to high
Generates pulse when transition occurs

## Slide 6: Flip-flop
Also known as Set-Reset trigger, RS-trigger, RS-latch, etc
Detects and remembers change in R and S signals
Edge-triggered (like edge detector)

## Slide 7: D-trigger
Remembers value of D when clock is high
When D changes on high clock, we have problem

## Slide 8: Master-slave latch
Two D-triggers connected sequentially, with inverted clock
First trigger latches D on high clock
Second trigger latches stable value of (Q) on low clock

## Slide 9: MSL timing diagram

## Slide 10: Other interesting devices
Edge-triggered D-latch http://www.falstad.com/circuit/e-edgedff.html
JK-trigger http://www.falstad.com/circuit/e-jkff.html
4-bit ripple counter built on JK-triggers http://www.falstad.com/circuit/e-counter.html
4-bit synchronous counter (simplified carry lookahead) http://www.falstad.com/circuit/e-synccounter.html
Decimal (BCD) counter http://www.falstad.com/circuit/e-deccounter.html

## Slide 11: D-latch using CMOS PTL
Six transistors
The D-latch on logic gates used 22 transistors!

## Slide 12: Master-slave latch on PTL

## Slide 13: Multiported register

## Slide 14: Multiport register features
Multibit storage (4 bit on previous slide)
Controlled latching. Has clock and Enable signals.
  In CdM-8, most instructions operate on a single register.
  Other registers must remain unchanged.
Multiple three-state outputs
  In CdM-8, only selected register values are needed on each clock
  Using three-state outputs, we can attach all registers to a single bus or to several buses

## Slide 15: Finite state machine
A formal computation model
Used in many branches of computing
  Network protocols
  Parsers and lexers
  Event-driven programming
  Hardware design
  etc
Formally, any digital device (including von Neumann computer) is a Finite State Machine
Can be represented as graph of states and transitions
Can be directly implemented in hardware

## Slide 16: Hardware FSM

## Slide 17: One possible next step: microprogramming

## Slide 18: Microprogramming
Most modern CPU are actually microprogrammed machines
Many peripherial computer devices (those which do not have it’s own CPU inside) also are implemented as microprogrammed machines or FSM
But we won’t go into this now