## Slide 1: Lecture 3 Conditions and branches
Computing platforms
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2018

## Slide 2: CdM-8 flag semantics
N – sign bit of the result. Used for signed comparison
C – carry bit of the result. Used for unsigned comparison
Z – result is zero. Used for signed, unsigned and bitwise comparison
V – signed overflow (sign loss). Can be used to catch errors
V is also needed for correct signed comparison

## Slide 3: C and unsigned subtraction/comparison again
Subtraction  adding 2’complement
When the result < 0, C is 0
1-255 = 1+0000 0001 = 2
When the result > 0, C is 1
3-2 = 11+1111 1110 = 1+C

## Slide 4: Full list of CdM-8 branch instructions

## Slide 5: More about branches
In typical assembler, branch is like goto statement.
You must invent label names and jump to labels
Typical equivalent of if (condition) { then-block } else {else-block) requires one comparison, two labels, one branch and one jump
(unconditional branch)
Condition calc
b[!cond] $1
Then-block
Br $2
$1: Else-block
$2: …

## Slide 6: CdM-8 assembler has richer syntax
If
  Calc condition
is cond
  Then-block
Else
  Else-block
Fi

## Slide 7: Real example
if tst r0
is z ldi r1, 10
add r1, r0
else
shla r0
fi
Consult tome.pdf for syntax for complex conditions
(it is not so elegant)

## Slide 8: Loops
# r2=r0*r1 (assuming r1 is non-negative)
clr r2
while tst r1
stays gt
add r0, r2
dec r1
wend

## Slide 9: Post-condition loop
# find a zero
ldi r0, array-1
# Initialise r0 to point to the cell before the first element of the array.
do
inc r0 # point r0 to the next element
ld r0, r1 # read the element into r1
tst r1 # examine it
until z # if r1 is 0 then exit, otherwise continue

## Slide 10: Nesting of if’s and loops is possible
You can use them like blocks in high-level languages
You do not need to invent label names
You do not need to worry about correct nesting
Much harder to write spaghetti code (than with raw branches)
This is why CdM-8 assembly is called Platform 3 ½
Actually, it is much simplier to implement than you probably think
It is all described in tome.pdf
Beware: in some exercises using structural statements is explicitly prohibited