## Slide 1: Lecture 4 Multiplication and division
Computing platforms
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2018

## Slide 2: Multiplication by adding
A*B
P=0
While B>0 do
P+=A
B--
Wend
For 8-bit values, 256 additions in worst case
For 64-bit values on modern CPU, won’t finish in your lifetime

## Slide 3: Let’s consider special cases
A*2 = A+A = lshift(A,1)
A*2N = while N-->0 do P+=A wend = lshift(A,N)
A*(2N+2M)=A*2N+A*2M
If we represent arbitrary number as sum of 2N…

## Slide 4: Algorithm of multiplication
Any number has the binary representation
B=Sum(b[N]*2N), where b[N] - Nth bit of binary representation
P=A*B=Sum(A*b[N]*2N)
So, the algorithm
N=0
P=0
While N<bits(B) do
P+=A*b[N]
A=lshift(A,1)
Wend

## Slide 5: Let’s try to visualize it
Note that 4-bit*4bit
yields 8-bit result

## Slide 6: Looks familiar?

## Slide 7: How to implement this in CdM-8?
b[N] can be calculated as series of right shifts
Shr instruction shifts the register and moves lowest bit to C
We do not need to count to 8
The loop can stop when reg==0 (Z flag is set)
But how to calculate 16-bit P and 16-bit A*2N?
They need 2 registers each, and we have only four registers.

## Slide 8: Let’s go in other direction
N=7
P=0
While True do
P+=A*b[N]
if N==0 break
P=rshift(P,1)
N--
Wend
Now we need a register to store N
Or we can unroll the loop (there are only 8 iterations after all)

## Slide 9: Demonstration in CocoIDE
http://ccfit.nsu.ru/~fat/Platforms/mult.asm
8-bit unsigned multiplication witn 16-bit results using only registers (no memory access)

## Slide 10: What about signed multiplication?
If we treat 1101 and 1110 as
two-complement signed numbers, the result is wrong.
You do not even need to convert to decimal.
The operands are both negative, but the result is positive!

## Slide 11: Proper way of two-complement signed multiplication
Sign-extend both numbers
before the multiplication
Actually, this is a disadvantage
of two-complement presentation
With sign-magnitude, you just
multiply unsigned and xor sign bits

## Slide 12: Division
the dividend is the number to be divided
the divisor is the number the dividend is divided by
the quotient is the main result of division,
a remainder, which is the quantity left over, i.e. the difference between the dividend and product of the quotient and the divisor.

## Slide 13: Exact definition of quotient
a quotient, which is the whole number of times the divisor ‘goes into’ the dividend.
In other words, the quotient is the maximum integer that if multiplied by the divisor gives the result not exceeding the dividend.

## Slide 14: Let’s try to divide 11(dec) to 3(dec)
11÷3=3 rem 2
11(dec)=1011
3=0011