## Slide 1: Lecture 10 Macros
Computing platforms
Novosibirsk State University University of Hertfordshire
D. Irtegov, A.Shafarenko
2018

## Slide 2: Repeating command sequences
ldi r0, label
ld r0, r0
This sequence is repeated in many programs over and over
In some ISA (CISC processors), there is a single command for this,
But CISC hardware is much more complex
Can we make a single [pseudo]instruction in software?

## Slide 3: Yes we can
macro ldv/2
ldi $1, $2
ld $1, $1
mend
ldv is macro (pseudo instruction) name
/2 is number of parameters
$1 and $2 are parameters
ldv r0, label

## Slide 4: Macro (macro definition)
Macroprocessing is essentially a text substitution
ldv r0, label
$1=r0, $2=label
macro ldv/2 ldi $1, $2 ld $1, $1 mend | # macro ldv/2 ldi r0, label ld r0, r0 # mend

## Slide 5: Macroprocessing
Substituting macros happens before or during compilation
  Unlike subroutine call which happens at runtime
Logically, it is always happens before compilaton,
because result of macro substitution is compiled like normal code
But the result of substitution can contain other macros…
Many macro languages do not support recursive macros
And practically none allow forward macro reference
I.e. you always must define a macro before it can be used (unlike label or subroutine)

## Slide 6: Why use macros?
To make your program shorter (== easier to read)
To make names for common idioms (instruction sequences)
To avoid copy-paste code reuse
Why copy-paste code reuse is bad?
  If you find error in copypasted code,
  you must find all copies
  and fix them separately

## Slide 7: Names for common idioms
macro clr/1. # clear a register
xor $1, $1
mend
macro test/1. # set Z and N flags according to register values
mov $1, $1
mend
macro bnle/1
bgt $1
mend

## Slide 8: How not to use macros
macro incmem/1
ldi r0, $1
ld r0, r1
inc r1
st r0, r1
mend
Looks good, but uses two registers
And we cannot avoid this

## Slide 9: How not to use macros (continue)
macro incmem/1 # “safe” version
push r0
push r1
ldi r0, $1
ld r0, r1
inc r1
st r0, r1
pop r1
pop r0
mend

## Slide 10: Why it is a bad idea?
incmem a
incmem b
Result of this macro substitution would have
  two extra push and
  two extra pop
No good for a machine with 256 bytes of memory!
Compilers often have so called peephole optimization
  finding redundant commands in compiled code and removing them
But assemblers usually literally assemble anything you wrote

## Slide 11: So, macro is not universal tool
It has strong limitations
Sometimes, people are saying “compilers are just advanced macroprocessors”, but this is not correct
Compilers (Level 4 platforms) are much more complex entities than macroprocessors
But macros are simple and powerful (if used with judgement)
There are pretty complex languages implemented as macros (LaTeX for example)

## Slide 12: Nonce (apostrophe after a label name)
macro strcpy/2
push r2
push $1
push $2
loop’: ld $1,r2
inc $1
st $2,r2
inc $2
move r2,r2
bne loop’
pop $1
pop $2
pop r2
mend

## Slide 13: What if one of parameters will be r2?
unique $1,$2,temp
push ?temp
Unique directive selects a register which is different from $1 and $2
temp will be local symbol inside of the macro definition
? designates reference to such a symbol
If we use ?temp instead of r2 in strcpy macro, it won’t conflict with parameters
Unique is not the only way to generate such symbols

## Slide 14: Wait, there is more!
Actually, CdM-8 “3 1/2” constructs, like if and while, are macros
if cmp r0,r1 is le move r0,r2 else move r1,r2 fi | cmp r0,r1 bgt else move r0,r2 br done else: move r1,r2 done:

## Slide 15: But how???
It is easy to prove that you cannot implement if-is-fi by simple text substitution (even with help of nonce and unique)
To implement if-is-fi macros, you need to
  Invent an unique name for a label
  Remember it (somehow transfer it between is and fi macro definitions)
  For if-is-else-fi, you need two unique labels
  And how do you do nested if?

## Slide 16: Nonce and unique are not enough!
macro if/0
mpush _’
mend macro is/1
mpop id
mpush alt?id
bn$1 alt?id
mend
macro else/0
mpop where
mpush new?where
br new?where ?where: mend macro fi/0 mpop term
?term: mend

## Slide 17: How it all works?
mpush and mpop are operations on macro stack
Macro stack is a LIFO memory existing at compilation time
mpush and mpop are directives, not instruction mnemonics
mpush _’ engages a nonce and pushes it to stack

## Slide 18: Let’s see this on the example
macro if/0 # MS is short for [top of] Macro Stack
mpush _’ # MS=_1
mend macro is/1
mpop id # id=_1
mpush alt?id # MS=alt_1
bn$1 alt?id
mend
macro else/0
mpop where # where=alt_1
mpush new?where # MS=newalt_1
br new?where ?where: # label will be alt_1 mend macro fi/0 mpop term # term=newalt_1 or alt_1 (without else)
?term: # label will be newalt_1 or alt_1 mend

## Slide 19: But what about loops?
Loops have break/continue which can be used inside of the if blocks
Break and continue cannot just pop the label from top of the stack
To deal with this, loops use second macro stack, referenced by 1mpush and 1mpop directives
Actually, there are three macro stacks in CdM-8 assembler

## Slide 20: Another pair of useful macros
Save and restore
save r1
save r2
save r3
do something with r1,r2,r3
restore
restore
restore
Much harder to restore registers in wrong order!